LNP Problem/Issue Identification and Description Form

Submittal Date (mm/dd/yyyy):  07/9/2019

Company(s) Submitting Issue: iconectiv (LNPA)

Contact(s):  Name Patrick K. White_

Contact Number 7 3 2 /6 9 9 /4985

Email Address   pwhite@iconectiv.com

(NOTE: Submitting Company(s) is to complete this section of the form along with Sections 1, 2 and 3.)

- Problem/Issue Statement: (Brief statement outlining the problem/issue.)

The XML Interface Specification (XIS), currently does not specify the Content Type to be used in interface messages except in the message examples.  Since multiple Content Types can be used and have been implemented, the XIS should be updated to identify the supported Content Type(s) other than in example messages.  This will make the implementation clear to any vendor that wants to build the XML interface in the future.

- Problem/Issue Description: (Provide detailed description of problem/issue.)

The XIS does not specify the Content Type(s) supported by the Current NPAC SMS implementation.  The Content-Type is only identified in example messages in the XIS.  This does not represent the Content Types actually supported.  Although all of the message examples display a Content Type of “text/xml”, the NPAC SMS supports both “text/xml” and “application/xml” Content Types.

Standards (IETF RFC 3023) identifies that Media Type of “text/xml” should be used when the source XML document is readable by casual users, otherwise “application/xml” is preferable.  But a newer standard (IETF RFC 7303) obsoletes RFC 3023 in standardizing “application/xml” (and other “application” Media Types) while defining “text/xml” as an alias for the respective “application/xml” Media Type.

The iconectiv NPAC SMS implemented support for both “text/xml” and “application/xml” as follows on the XML interface: either “text/xml” or “application/xml” will be accepted as Context Types on XML interface messages sent by SOAs and/or LSMSs to the NPAC SMS.  NPAC SMS will only send messages to SOAs and LSMSs with a Content Type of “application/xml”.

B.   Frequency of Occurrence:

Very Infrequent – could cause issues when a vendor attempts to initially implement the XML interface.

- NPAC Regions Impacted:

Mid Atlantic ___ Midwest___ Northeast___ Southeast___ Southwest___ Western___

West Coast___  ALL X

D.  Rationale why existing process is deficient:

Unclear Requirements

E.   Identify action taken in other committees / forums:

N/A

F.   Any other descriptive items:

N/A

- Suggested Resolution:

Update the XIS document to identify the applicable Content Types supported by the current NPAC SMS.  Update all message examples for messages sent from the NPAC SMS to local systems using a Content Type of application/xml.

- Final Resolution:

This issue resulted in the creation and acceptance of a NANC Change Order.  For further detail refer to the NANC Change Order(s) identified in the Related Documents field below.

LNPA WG: (only)				Final Resolution: 2/25/20

Item Number: PIM 126 v2			Related Documents: NANC 548

Issue Resolution Referred to: _________________________________________________________

Why Issue Referred: __________________________________________________________________ ____________________________________________________________________________________________________________________________________________________________________________